## Slide 1
FOM Analysis Design, Build, Fly!
9/15/13

## Slide 2: Missions Review
  Backcountry Rough Field Bush Plane
  Pre-Flight Rough Field Taxi Mission
  Mission 1 – Complete as many laps as possible in 4 minutes
  Mission 2 – 3 lap max load flight – 6”x6”x6” wood blocks
  Mission 3 – Emergency Medical Mission – 3 lap, prescribed load
  Competition in Wichita, KS

## Slide 3
Scoring Analysis Conclusions

## Slide 4: Design Drivers
Scoring Analysis Conclusions
Sample Competition Scenarios
Fast and Light Plane
Large Towing Capacity
Renaissance Plane
M1 = 1.7 – M2=1.5 – M3=5.8
RAC=2.5
Final Score = 324
M1 = 1.1 – M2=4 – M3=4
RAC=4
Final Score = 204.75 -- (if RAC=5, Score=163.8)
M1 = 1.45 – M2=3 – M3=5
RAC=3.5
Final Score = 243.00
Primary: Empty Weight
Secondary: Speed

## Slide 5: Figure of Merit Weights
 | Weight | High Lift/Short TO | Glide Capability | Size | Ease of Construction | Stability & Control | Payload Capability | Totals | Weight (%)
Weight | 0 | 3 | 2 | 4 | 4 | 4 | 4 | 23 | 18.25
High Lift/Short Takeoff | 3 | 0 | 2 | 2 | 2 | 1 | 3 | 12 | 9.5
Glide Capability | 4 | 4 | 0 | 4 | 5 | 3 | 5 | 24 | 19.06
Size | 2 | 4 | 2 | 0 | 2 | 2 | 2 | 14 | 11.12
Ease of Construction | 2 | 4 | 1 | 4 | 0 | 1 | 2 | 14 | 11.12
Stability & Control | 2 | 5 | 3 | 4 | 5 | 0 | 4 | 23 | 18.25
Payload Capability | 2 | 3 | 1 | 4 | 4 | 2 | 0 | 16 | 12.7
 |  |  |  |  |  |  |  | 126 | 

## Slide 6: Figure of Merit Weights
Figure of Merit | Weight (%)
Weight | 
Short-Take Off/High Lift | 
Speed | 
Size | 
Payload Capability | 
Stability & Control | 
Ease of Construction | 

## Slide 7: Wing Configuration
Wing Configuration | Weight (%) | Monoplane | Biplane | Tandem Wing / Canard | Flying Wing / Blended Body
Weight | 18.25 | 4 | 3 | 3 | 5
High Lift/Short Takeoff | 9.5 | 3 | 4 | 3 | 3.5
Speed | 19.06 | 4 | 2 | 3 | 4.5
Size | 11.12 | 3 | 1 | 3 | 4
Ease of Construction | 11.12 | 5 | 2 | 2 | 1
Stability & Control | 18.25 | 4.5 | 3 | 2 | 1
Payload Capability | 12.7 | 3 | 3 | 3 | 1.5
Total | 100% | 3.87 | 2.57 | 2.71 | 3.03

## Slide 8: Motor Configuration
Motor Configuration | Weight (%) | Mono Tractor | Mono Pusher | Twin Tractor | Twin Pusher | Tractor & Pusher
Weight | 18.25 | 4 | 4 | 2 | 2 | 2
High Lift/Short Takeoff | 9.5 | 4 | 2 | 5 | 1 | 2
Speed | 19.06 | 4 | 3 | 5 | 4 | 4
Size | 11.12 | 3 | 3 | 2 | 2 | 2
Ease of Construction | 11.12 | 5 | 3 | 2 | 1 | 1
Stability & Control | 18.25 | 4 | 2 | 3 | 1 | 1
Payload Capability | 12.7 | 3 | 3 | 3 | 3 | 3
Total |  | 3.87 | 2.86 | 3.17 | 2.12 | 2.21

## Slide 9: Tail Configuration
Empennage Configuration | Weight (%) | Conventional Tail | V-Tail | Single Vertical Stabilizer | Winglets
Weight | 18.25 | 4 | 4 | 3 | 5
High Lift/Short Takeoff | 9.5 | 5 | 5 | 1 | 2
Speed | 19.06 | 3 | 4 | 3 | 4
Size | 11.12 | 3 | 3 | 4 | 5
Ease of Construction | 11.12 | 5 | 2 | 5 | 5
Stability & Control | 18.25 | 5 | 2 | 1 | 1
Payload | 12.7 | 3 | 3 | 3 | 3
Total | 100% | 3.96 | 3.27 | 2.78 | 3.54

## Slide 10: Landing Gear Configuration
Landing Gear Configuration | Weight (%) | None | Trike | Skids | Retractable | Tail Dragger | Mono Wheel
Weight | 18.25 | 5 | 3 | 4 | 1 | 3.5 | 4
High Lift/Short Takeoff | 9.5 | 1 | 3 | 1 | 3 | 3 | 2
Speed | 19.06 | 5 | 3 | 4 | 3.5 | 3.5 | 4
Size | 11.12 | 5 | 3 | 3 | 1 | 3.5 | 3
Ease of Store Construction | 11.12 | 5 | 5 | 3 | 1 | 4 | 3
Stability & Control | 18.25 | 0 | 5 | 1 | 3 | 2 | 1
Total | 100 | 3.07 | 3.2 | 2.4 | 1.9 | 2.8 | 2.5

## Slide 11: Control Surface Configuration
Control Surface Configuration | Weight (%) | 2x Ailerons, 2x Elevator, 2x Flaps | 2x Ailerons, 1x Elevator, 2x Flaps | 2x Ailerons, 2x Elevator | 2x Elevons
Weight | 13.10 | 1 | 2 | 3 | 5
High Lift/Short Takeoff | 9.52 | N/A | N/A | N/A | N/A
Glide Rate | 16.67 | 3 | 3 | 3 | 3
Size | 9.52 | N/A | N/A | N/A | N/A
Ease of Construction | 9.52 | N/A | N/A | N/A | N/A
Stability & Control | 14.88 | 5 | 4 | 4 | 2
Payload Capability | 10.12 | N/A | N/A | N/A | N/A
Climb Rate | 16.70 | 5 | 5 | 5 | 4
Total | 100% | 3.5 | 3.5 | 3.75 | 3.5

## Slide 12
Graduate Advisors
Annie Legault
Tamuto Takakura
University of Notre Dame
AIAA DBF
Faculty Advisor
TBD
Pilots
Terry Rensberger
Paul Distler
Team Leads
Harrison Yates
Eliseo Miranda
Report Lead
Eliseo Miranda/Harrison Yates
Structures / CAD Lead
Keldan Mulvey
Propulsion / Electronics Lead
Joshua Vahala
Aerodynamics Lead
Kate Disser
TBD
TBD
Construction/Testing Lead
Tom Paulius
TBD
2013-2014
TBD
TBD

## Slide 13: Organization
All students now have 50GB worth of cloud storage within Box
  https://notredame.box.com/files
  Invites to the DBF “Box” will be sent shortly
    Used for all team data storage (Report files, CAD files, pictures, etc.)
Machine Shop Training
  Laser Cutter, Safety, 3D Printer
Weekly Meetings
  Sunday @ 4:30pm
  Stinson-Remick 109

## Slide 14: Notre Dame Design/Build/Fly
Questions?